# Test Objectives
To validate the attitude control system's performance
- Verify the system's ability to achieve desired attitude and angular rates
- Test the momentum management system's effectiveness
- Evaluate system response to disturbances
# Test Environment
The satellite is moving in a circular orbit around Earth at an altitude of 600 km.
The satellite contains sensors capable of measuring attitude and angular velocities.
Reaction wheels in a pyramidal configuration are used for actuation. (max torque = 0.015 Nm, Max momentum = 0.035 Nms)
A sinusoidal disturbance torque of 10^-6 Nm exists in each direction (random phase difference).
# Test cases
The ability of the AOCS to steer the satellite from [0,0,0] deg attitude, [15, -15, 15] deg/s angular velocity to [30, 50, 70] deg attitude and < [0.2, .2, 0.2] deg/sec angular velocity , for different conditions is going to be evaluated based certain criteria.
1. Assuming no error in sensor measurements and no disturbance torques.
2. With disturbance torques
3. With gaussian sensor noise ( [0.01;0.01;0.01] deg in attitude, [0.001;0.001;0.001] deg/s in rate
4. With disturbance torques and sensor noise
# Success criteria
1. Pointing accuracy of 1 deg.
2. Angular velocity < [0.2,0.2,0.2] deg/sec
3. Setting time of < 8	00 seconds
4. Reaction wheel momentum and torques below saturation
# Data collection
- Attitude (Euler angles and quaternions)
- Angular velocities
- Angular momentum
- Reaction wheel – momentum and torque provided by each wheel
- Unloading torque (if any)
# Potential challenges
## Reaction wheel modeling
- Modeling non-linear effects such as friction, imbalance, and bearing imperfections
- Representing the pyramidal configuration accurately and its impact on torque distribution
## Satellite Dynamics modeling
Modeling the coupling effects between different axes due to off-diagonal terms in the MOI matrix.
## Noise modeling
- Modeling additional disturbances not explicitly mentioned (e.g., solar radiation pressure) for a more realistic simulation
- impact of temperature variations on sensor and actuator performance and the effects of radiation on electronic components
- Modeling gyroscope noise and bias for angular rate measurements
- Implementing sensor fusion algorithms to combine data from multiple noisy sources
## Computational challenges
Ensuring real-time or near-real-time performance for SILS testing
Handling numerical precision issues, especially for small disturbance torques (10^-6 Nm)

Outline Test Cases
a) Nominal operation:
- Reorientation from initial to final attitude
- Maintaining desired angular rates
  b) Disturbance rejection:
- Response to sinusoidal disturbance torque
  c) Momentum management:
- Wheel speed control and momentum redistribution
- Unloading procedure (if implemented)
  d) Edge cases:
- Maximum slew rates
- Near-saturation of reaction wheels
Describe test envireonment
- Simulink model of satellite dynamics and reaction wheels
- Simulated sensor inputs (e.g., star tracker, gyros)
- Simulated actuator outputs (reaction wheel torques)
Define Test Procedures:
For each test case, outline:
- Initial conditions
- Test duration
- Expected outcomes
- Pass/fail criteria
Identify Potential Challenges:
- Hardware modeling accuracy (e.g., reaction wheel dynamics, sensor noise)
- Environmental disturbance modeling
- Computational limitations of real-time simulation
Data Collection and Analysis:
- Specify data to be logged (attitude, rates, wheel speeds, torques)
- Define analysis methods to evaluate system performance
Test Execution Plan:
- Describe how tests will be run (e.g., automated scripts, manual execution)
- Outline any required pre-test calibrations or checks
Reporting:
Define the format for test results and analysis reports
Validation and Verification:
Describe how test results will be validated against requirements
To implement this plan in your project:
1. Create a separate Simulink model for SILS testing, incorporating:
  1. Your existing attitude control system
  2. More detailed hardware models (e.g., sensor noise, actuator dynamics)
  3. A comprehensive disturbance model
2. Develop MATLAB scripts to:
  1. Initialize test cases
  2. Run simulations
  3. Collect and analyze data
3. Implement automated checks for pass/fail criteria
4. Create visualization tools for test results

discuss the challenges you anticipate, such as accurately modeling hardware behavior and environmental disturbances, as required by the assignment . This SILS test plan will demonstrate your understanding of the validation process for attitude control systems and show how you would prepare for real-world implementation of your design.